Inter vlan routing:

normally a vlan cant communicate with other vlan unless there is inter vlan routing
in intervlan routing there are many process to do so.

In here we use a router on a stick method
and we use a router sub interfaceto do inter vlan routing
1) first we create three vlan red,blue and green
2)then we add a router with the switch
3) then each sub interface ip will be the the vlan ip
4) then we have to configure and encapsulte thing thing

first step:

1) attach 6 pc with the switch and group it 2 computer
2)so there is three group
3) then give ip just like this

first vlan

pc1->192.168.0.10
pc2->192.168.0.20
gateway:192.168.0.100
second vlan:

pc3->192.168.1.10
pc4->192.168.1.20
gateway:192.168.1.100
third vlan:

pc5->192.168.2.10
pc6->192.168.2.20
gateway:192.168.2.100
then go to the switch and create vlan

Switch(config)#vlan 10
Switch(config-vlan)#name blue
Switch(config-vlan)#exit
Switch(config)#vlan 20
Switch(config-vlan)#name green
Switch(config-vlan)#exit
Switch(config)#vlan 30
Switch(config-vlan)#name yellow
Switch(config-vlan)#exit

Switch(config)#int range fastEthernet 0/1-2
Switch(config-if-range)#switchport mode access
Switch(config-if-range)#switchport access vlan 10
\
Switch(config-if-range)#exit
Switch(config)#interface vlan 20

Switch(config-if)#exit
Switch(config)#int range fastEthernet 0/3-4
Switch(config-if-range)#switchport mode access
Switch(config-if-range)#switchport access vlan 20

Switch(config-if-range)#exit
Switch(config)#int range fastEthernet 0/5-6
Switch(config-if-range)#switchport mode access
Switch(config-if-range)#switchport access vlan 30
Switch(config-if-range)#exit
Switch(config)#do sh vlan

now this port bellow 0/20 is the port where router connected with the switch ad we have to configure it with mode trunk

Switch(config)#interface fastEthernet 0/20
Switch(config-if)#switchport mode trunk

the work with the switch is over now we have to configure the router

in router we select an interface then 3 subinterface it and give ip the ip will
be the corresponding gate way ip of the pc

router command:

Router#configure terminal

Router(config)#interface gigabitEthernet 0/0
Router(config-if)#no shut

Router(config)#int gigabitEthernet 0/0.10
Router(config-subif)#encapsulation dot1Q 10 //this 10 is the vlan id
Router(config-subif)#ip address 192.168.0.100 255.255.255.0
Router(config-subif)#no shut
Router(config-subif)#exit

Router(config)#int gigabitEthernet 0/0.20
Router(config-subif)#encapsulation dot1Q 20
Router(config-subif)#ip address 192.168.1.100 255.255.255.0
Router(config-subif)#no shut
Router(config-subif)#exit
Router(config)#interface gigabitEthernet 0/0.30
Router(config-subif)#encapsulation dot1Q 30
Router(config-subif)#ip address 192.168.2.100 255.255.255.0
Router(config-subif)#no shut

now ping any pc of any vlan to another vlan